XDENU 2.0 DOCUMENTATION
-----------------------

INDEX

	0.5. What's new in Xdenu 2.0.
	1.0. What is Xdenu
	2.0. Linux operating system, X windows and XFree86
	3.0. Installing Xdenu 2.0
		3.1. Xdenu 2.0 distribution set
		3.2. Preliminary information needed
		3.3. How Xdenu 2.0. works?
		3.4. System requirements
		3.5. Installation 
	4.0. What do you get?
	5.0. Using Xdenu
		5.1. Booting the computer
		5.2. Making backups
		5.3. Mounting the hard drive
		5.4. Networking
		5.5. Virtual terminals
		5.6. Closing the X session
		5.7. Using Umsdos file system
        6.0. Upgrading with modules
		6.1. Upgrade
		6.2. Current modules: Xkit, Netkit, Termkit, Pppkit
		     and Mankit
		6.3. Making new modules
		6.4. The way upwards
	7.0. Security
	8.0. Authors' comments
	9.0. Bugs
	10.0. Post Scriptum

0.5. What's new in Xdenu 2.0.

	  I. Umsdos - Xdenu Linux uses DOS fat file system
	 II. SCSI hard disk support added
	III. Swapping (paging) supported
	 IV. VGA16 X server supported
	  V. Package divided in modules 
	 VI. Mouse configuration bug fixed
	VII. passwd added 
       VIII. man - manual pages	
         IX. mtools - use of DOS floppies made easy
          X. mke2fs - create Linux file system
	 XI. bash - more intelligent shell
        XII. X fonts - more fonts added  

1.0. What is Xdenu

	Xdenu 2.0 is  a  small Linux operating system  distri-
	bution kit.  System can be upgraded to a complete one.
	X  terminal    capabilities, networking   software and
	multi-session modem software  are provided as separate
	modules.  Main  goals have  been  the ease of  use and
	small size.  All  configuration is done by dialogs and
	minimum disk space  needed  with X is approximately  4
	MB.  See Section 2.0 for getting information on Linux.

	The  authors   have tried  to   establish an X Windows
	terminal environment  with minimal  space requirements
	and best possible  performance.  This package has been
	created after an initiative  in local Linux news group
	for  use  in  the  Helsinki University   of Technology
	campus local area network.  The  intent is to give all
	network users easy X access.

	This  package is freely  distributable.  This document
	should  be  included  in all  copies.   Bug fixes  and
	comments can be sent to xdenu@cs.hut.fi.

	Xdenu aims never to  be a respectable package.  No up-
	dates are promised.  The  user is responsible for  the
	security of  the system  as well as  possible hardware
	and software  failures during installation  and opera-
	tion.

	X  Window System is  a  trademark of the Massachusetts
	Institute  of Technology.  See   section 2.0.  Most of
	the software is  covered   by the GNU  General  Public
	License  and so the  source code  have to be available
	freely.  We have   taken the binaries from   Slackware
	1.2.2 and sources of Slackware are available from

	ftp://ftp.cdrom.com/pub/linux/slackware_source

	Jump  to chapter 3 if you  want to install Xdenu imme-
	diately.

2.0. Linux operating system, X Windows and XFree86

	For   detailed  description   of   Linux,   get  Linux
	Information  Sheet   (INFO-sheet) and   META-FAQ  from

	ftp://nic.funet.fi/pub/OS/Linux/doc/INFO-SHEET
	ftp://nic.funet.fi/pub/OS/Linux/doc/META-FAQ*

	or

	ftp://sunsite.unc.edu/pub/Linux/docs/HOWTO/INFO-SHEET
	ftp://sunsite.unc.edu/pub/Linux/docs/HOWTO/META-FAQ

	See preformatted manual page  for X windows  (X.1x) in
	some UN*X system.  Manual pages are in mankit package.

	For  more information  see the XF86VidDoc.tar.gz  XF86
	Video   documentation package.   File XFree86.man con-
	tains general   information and Xconfig.man  describes
	the syntax of the Xconfig file.

3.0. Installing Xdenu 2.0

	The  busy reader can  study only this chapter and skip
	the rest. Closer investigation  of the sub-chapters is
	highly    recommended afterwards.   Minimum     system
	requirements are 386 processor,  4MB memory,  4MB disk
	space on  DOS  fat partition.    No repartitioning  is
	needed.   File linuz.exe  is  self-extracting  archive.
	Resulting system in directory  \linux is ready to run.
	All you have to do is to check

		\linux\etc\loadlin\linux.bat

	to start the system.  

	3.1. Xdenu 2.0 distribution set

	The basic package  of  Xdenu  consists  of one   self-
	extracting archive.    There are   two   possibilities
	available,

		      linuz.exe and linuzs.exe
	
	The latter  executable  has a kernel with SCSI support.
	Both systems work fine in a computer which has only an
	IDE interface.  The usage of linuz.exe saves some disk
	space.

	The files included in this archive are enough to start
	the system from the hard disk.

	For  information in  kernel  configurations  see files
	ide-config.in   and scsi-config.in  for  ide  and scsi
	kernels respectively.

	3.2. Preliminary information needed

	All  the  information   needed to   install  the basic
	package is included  in this document file.  When  you
	upgrade the  system some more  information is  needed.
	See section 6.2. for description of each package.

	If you  are going to use  Xdenu in network environment,
	you need to know the TCP/IP networking parameters such
	as  your IP number, IP  number  of the nameserver etc.
	If  you use   also  X,  the X   font server   must  be
	specified.  Only basic fonts are included in Xdenu.

	3.3. How Xdenu 2.0. works?

	Xdenu  2.0  is  installed  on  a  top  of  the DOS fat
	file system using Umsdos.  Umsdos is a novel invention
	in the Linux   world, a file system   laying on a  DOS
	disk, which allows extended file names, symbolic links
	etc. without re-partition  of the disk.  This is  done
	by adding on each directory a data file

			--linux-.---

	which includes the characters and information that DOS
	can't  represent.   When using  Linux these  files are
	invisible, but if DOS is used, they can be seen.

	This kind of emulation causes a remarkable performance
	penalty and cannot be recommended for large scale use.

	For backuping and experimental use, however, this file
	system is very convenient.

	Another Linux  community  innovation  is   the loadlin
	program.  It allows the  booting of Linux from the DOS
	prompt without tampering with the master boot record -
	the thing that makes many computer owners shake.

	3.4. System requirements

	For Linux  a minimum requirement  is a computer with a
	386SX processor.

	Most memory  limitations have disappeared after adding
	the swapping (i.e.  paging) support.  Some of the free
	disk  space can   now  be  reserved as  a   swap file.
	However, at least 4 MB of physical  memory and 4 MB of
	swap space is needed, if Xdenu X terminal capabilities
	are going to be used.

	The basic binaries set will take  about 3 Megabytes of
	hard disk space.

	Xdenu  2.0  is  supporting SCSI.  Check scsi-config.in 
	for kernel compilation options.

	3.5. Installation 

	(1) Choose the correct basic package and the upgrade 
	    modules for your computer.
	(2) Open the self-extracting archive on a hard disk,
	    where you want to add Linux.  Remember, that you
	    have to be in the root directory (\) of your disk.
	(3) Check that \linux\etc\loadlin\linux.bat is in order.
            There should be a correct drive letter pointing
	    at your linux disk.
	(4) Run linux.bat
	(5) Login as root and run setup
	(6) Add modules and rerun corresponding setup
	    scripts for re-configuration, if needed
	(7) Enjoy

	After installation  you can  restart Linux by running
	linux.bat from DOS prompt.

	The setup system that  Xdenu uses is far from perfect.
	It   uses   standard  VESA  definitions  and  aims  to 
	minimize the  changes  the  user  needs  to do.  Setup 
	scripts  have  functioned  without  errors in authors' 
	computers.  These scripts have successfully configured 
	network and  X  Windows and no  further  modifications 
	have been necessary.

	Nevertheless, the authors can't  guarantee that in all 
	circumstances this is the case.  The user should check  
	the parameters  created by the automated scripts.  For 
	further  information  and  trouble shooting Ethernet-
	HOWTO and XFree86-HOWTO are available from

	ftp://sunsite.unc.edu/pub/Linux/docs/HOWTO/Ethernet-HOWTO
	ftp://sunsite.unc.edu/pub/Linux/docs/HOWTO/XFree86-HOWTO

4.0. What you get ?

	32  bit Linux  multitasking  multiuser  environment
	plus programs:

	Linux System:
	agetty, ctrlaltdel, halt, init, reboot, shutdown, 
	update

	System protection:
	passwd

	System status:
	free, top

	Shells:
	bash, sh	

	Setup:
	dialog, keyconfig, netconfig, setup, swapconfig, 
	timeconfig, upgrade, xconfig

	Handling disks:
	e2fsck, fdisk, mke2fs, mkswap, mount, swapoff, swapon, 
	umount,	sync, umssync

	Basic networking:
	ifconfig, route, ftp, telnet

	Handling files:
	cat, chmod, cp, compress, cut, fgrep, grep, gunzip, 
	gzip, head, less, ln, ls, mkdir, mv, rm, tail, tar, 
	uncompress, wc, zcat 

	Editing:
	elvis, vi --> elvis, sed

	Standard *n*x:
	basename, clock, date, dd, df, dirname, domainname, expr, 
	hostname, loadkeys, man, mknod, pwd, setterm, sleep, 
	test, tr, who, whoami

	X scripts:
	startx, xhelp

	Mtools for using DOS floppies:
	mattrib, mcd, mcopy, mdel, mdir, mformat, mlabel, mmd,
	mrd, mread, mren, mtools, mtype, mwrite

5.0. Using Xdenu

	5.1. Booting the computer

	In a multitasking  environment  several  programs  are
	executed at the  same time.  The operating system  has
	also disk  buffers in the  memory,  which contain data
	waiting to be written to  the disk.  These are some of
	the reasons why  shutting  down is a  complex process.
	For this purpose there is a special command, which you
	should use  when you want to  end your session.  It is
	called

		reboot

	You  should give  this  command  only  after you  have
	finished all your applications.  The rebooting takes a
	little  time and  you   can follow the system  sending
	signals to various programs.  When you see the message
	from your graphics adaptor it    is safe to turn   the
	power off.

	The  ctrl-alt-del  key sequence is  monitored by Linux
	and shortly after this    command has been  given  the
	rebooting  process   will   start.  This   is    fully
	equivalent to the reboot command given manually at the
	command prompt.

	5.2. Making backups

	If you  want to make  backups, you can  mount your DOS
	hard disk using mount command and simply copy files to
	some desired directory.   Backuping might be necessary
	for your configuration files.  Remember that  DOS file
	system uses only 8+3  characters for a file name. Also
	only capital letters   are  supported by DOS.    These
	problems   can be avoided, if  you  use Umsdos as file
	system type when running mount command  with a DOS fat
	drive.

	5.3. Mounting a hard drive

	CAUTION! Never mount  same partition again  i.e. don't
	try to mount again the partition where Xdenu resides.

	In Linux hard disks  are  treated as devices  and  the
	location  of the device files  is  the /dev directory.
	IDE  hard disks  are   devices /dev/hda and  /dev/hdb,
	which stand for the first  hard disk (BIOS C disk) and
	the  second hard disk (BIOS  D  disk) respectively.  A
	single hard  disk  is  usually  divided  into  several
	partitions. Each of  these partitions can be  accessed
	separately  and for  this   purpose there are  devices
	/dev/hda1, /dev/hda2,  /dev/hda3 etc.  for the C drive
	and /dev/hdb1, /dev/hdb2 etc. for the D drive.

	Likewise, SCSI    disks  are  denoted    /dev/sda  and
	/dev/sdb. The separate  partitions are identified with
	minor numbers just as  in the IDE  disks. The rest  of
	this chapter can be applied to SCSI  disks as well, by
	replacing strings "/dev/hd" with "/dev/sd".

	A partition can be  mounted on an empty  directory. In
	Xdenu there  is a  directory in  /  for  this purpose.
	This directory is:

		mnt  

	You can make   additional directories  for  your needs
	using mkdir command.  The   next task is to  find  the
	correct partition for mounting.  This  can be done  by
	using the fdisk program. Give the command

	xdenu # fdisk -l 

	The output should look like this:

	Disk /dev/hda: 14 heads, 62 sectors, 768 cylinders
	Units = cylinders of 868 * 512 bytes

	   Device Boot  Begin   Start     End  Blocks   Id  System
	/dev/hda1         203     203     767  245210    5  Extended
	/dev/hda2          14      14     202   82026   83  Linux native
	/dev/hda3           4       4      13    4340    1  DOS 12-bit FAT
	/dev/hda4   *       1       1       3    1271    a  OPUS
	/dev/hda5   *     203     203     462  112809    7  OS/2 HPFS
	/dev/hda6         463     463     500   16491+  82  Linux swap
	/dev/hda7         501     501     767  115877+  83  Linux native

	Disk /dev/hdb: 8 heads, 35 sectors, 872 cylinders
	Units = cylinders of 280 * 512 bytes

	   Device Boot  Begin   Start     End  Blocks   Id  System
	/dev/hdb1           1       1     586   82022+   6  DOS 16-bit >=32M
	/dev/hdb2         587     587     871   39900    5  Extended
	/dev/hdb5         587     587     871   39882+  83  Linux native

	This is  the partition table  of Centaur, the computer
	in which Xdenu 1.0 was constructed. We find that there
	are two DOS file systems we can use.  With the command

	xdenu # mount -t msdos /dev/hda3 /dos

	we mount the  dos boot  partition  on the /dos  direc-
	tory. Now  this partition can  be used for writing and
	reading  data.  After  finished, the  partition can be
	released by

	xdenu # umount /dos

	The proper  releasing procedure  is important, because
	otherwise the files might not  be written correctly on
	the  hard disk. The  reboot program  will take care of
	unmounting, if you forget to do it yourself.

	When you know  the  correct partition device  on  your
	computer, give the command

	xdenu # mount -t msdos /dev/hdXY /dos

	where  X stands for the correct   hard drive and Y for
	the partition number. The dos disk will be attached to
	your Linux file   system and you can  use  it as  your
	floppy disks.  Remember the  limitations of file names,
	though.

	Unmount it with

	xdenu # umount /dos

	5.4. Networking

	After installing Xkit, X Windows can  be used with the
	script startx. It  is  an interactive  program,  which
	first asks   the   session type and    then  makes the
	connection to the host desired.

	Telnet  is  added for   testing  and quick  networking
	purposes. For   file transfers ftp is  provided. These
	two programs are included also  in the basic  package.
	If no network use is expected, they can be removed.

	Termkit is a collection  of programs, which allow home
	Linux computer to  have a multi-session  connection by
	modem to another *n*x machine.

	Pppkit is full serial line IP connection kit.  You can
	use normal net programs (i.e. ncftp, telnet)  to  make
	connections  to other  computers.  Also  your computer
	has real ip-address.

	5.5. Virtual terminals

	While running  Linux in ASCII  mode, you can switch to
	another    terminal    by  pressing      keys   Alt-F?
	simultaneously, where ? can  be from 1  to 6. This way
	you can  have six sessions open at  the same time. Use
	the who command to see the users currently logged in.

	You can  also escape from the  X session back to ASCII
	mode by Ctrl-Alt-F?. X session is restored by Alt-F7.

	The  change of graphics  resolution can be done on the
	fly when using X.   The supported resolutions can   be
	scanned   upwards  and backwards  with  Ctrl-Alt-+ and
	Ctrl-Alt--. If the resolution used is smaller than the
	biggest    allowed by your    graphics  card  (usually
	1024x768), you can scroll the screen with the mouse.
 
	5.6. Closing the X session

	An X session  can be terminated by Ctrl-Alt-Backspace.
	This command kills the X server program and exits back
	to ASCII mode.

	5.7. Using Umsdos file system

	Umsdos remaps  the old DOS disk  root to /DOS in Linux
	directory hierarchy. This  is just a  way to represent
	things, nothing has   been changed physically.   Linux
	root directory,  /,   is the contents   of  DOS \linux
	directory.

	Every time Xdenu is booted,  it rescans the root  file
	structure using  umssync program. This  is done to fix
	possible  inaccuracies   in Umsdos file  structure. If
	user suspects an extra update  to be necessary because
	of some malfunction, he can use  the very same command
	manually in superuser mode by

	xdenu # umssync .

	In  normal use this is   not necessary, because  Linux
	will take care of the integrity of the file system.
	
6.0. Upgrading with modules

	6.1. Upgrade

	Upgrade is a small script, which Xdenu uses to add new
	modules to an existing Linux system. It is basically a
	user interface to the well-known Unix tar program.

	The  upgrading  happens simply by giving a command

	xdenu #	upgrade /DOS/file.tgz

	where file.tgz is the Xdenu module.
 
	6.2. Current modules: Xkit, Netkit, Termkit, Pppkit
	     and Mankit

	At the  moment  five  Xdenu modules exist.   They  are
	Xkit, Netkit, Termkit, Pppkit and Mankit.

	6.2.1. Xdenu module: Xkit

	Purpose: Allows X terminal connection
	Files: xkitm32.tgz xkitm8.tgz xkits3.tgz xkitsvga.tgz xkitv16.tgz
	Support: graphics cards ATi Mach32, ATi Mach8 and S3 chipsets
		 correspondingly, most SVGA cards in 256 color mode
		 and 16 color mode server. Only one file is needed.
	Binaries: XFree86 v.2.1.1 X server, basic fonts, configuration files
	Preliminary information: none, configured by scripts.
		 possible troubleshooting, see XFree86-HOWTO (3.5).
	Disk space: ~ 1.1 MB

	6.2.2. Xdenu module: Netkit

	Purpose: Extended networking
	Files: netkit.tgz
	Support: standard Linux
	Binaries: rlogin, rsh, finger, lynx, ncftp, nslookup, traceroute,
		  telnet, ftp
	Preliminary information: understanding of usage
	Disk space: ~ 650 kB

	6.2.3. Xdenu module: Termkit

	Purpose: multi-session connection to remote hosts by modem

	Files: termkit.tgz
	Binaries: minicom, sz, sz, rx, rz, term, trsh, tncftp, tfinger,
	          tmon, tupload, tredir, tftp, tlynx, manual pages,
	          sample configuration file
	Support: standard Linux, remote host must have a term server,
		 sources available e.g. from: 

		ftp://ftp.funet.fi/pub/OS/Linux/BETA/term
 
	Preliminary information: manual pages included
	Disk space: ~ 700 kB

	6.2.4. Xdenu module: Pppkit
	
	Purpose: IP networking over serial line
	Files: pppkit.tgz
	Binaries: chat, fix-cua, ppp-off, ppp-on, pppd, pppstats,
	          start-ppp, unlock, README files, manual
		  page
	Support: standard Linux, remote host must support
	         protocol
	Preliminary information: manual page and READMEs included
	Disk space: ~180 kB

	6.2.5. Xdenu module: Mankit
	
	Purpose: manual pages for all basic binaries
	Files: manpages.tgz
	Binaries: none
	Support: systems with gzip
	Preliminary information: none
	Disk space: ~180 kB

	6.3. Making new modules

	In addition to  the  data files, a module   consist of
	three short text files

		      comment   index   advice

	"comment"   describes  shortly   the  contents  of the
	archive file, "index"  contains the listing of archive
	files and finally "advice"  has a piece of advice what
	the user should do next. The existence of the "advice"
	file is not required, "comment" and "index" files have
	to be there.

	This Xdenu upgrade module structure is open and anyone
	who finds is usable can  adapt it. Also, the making of
	Xdenu upgrade modules is free -  if you find a program
	set, which might be usable for other Linux users, feel
	free to collect an Xdenu module and distribute it. The
	authors are interested to receive a copy too.

	Remember,  however, to  include the necessary document
	files or manual pages.

	6.4. The way upwards

	Xdenu offers  a solid basis  for upgrading to a larger
	Linux  system.   The basic  distribution set  includes
	fdisk for repartitioning of the  hard drive and mk2efs
	for creating   Linux second extended file  system. The
	pkgtool used in  Slackware  distribution can be copied
	in to the system and install Slackware packages.

7.0. Security

	Security issues  have been considered  and as a result
	no   login nor ftp  access   is allowed  to the  Xdenu
	system.  This  limitation   is   hard to break    from
	outside, because there's no  software support on Xdenu
	disks  for connections  from  outside.  However,  this
	software can be added later.

	Passwd  is included   for  protecting the    superuser
	mode.  You   can change  or  add  a password simply by
	giving the command

		passwd

8.0. Authors' comments

	After  releasing the first  version of Xdenu, we began
	to receive letters from  users.  It quite soon  turned
	out,  that  Xdenu was  not  the  first bugfree program
	package in the history of  linux-kind, although it was
	quite  close.  There was a minor  error  in the script
	which was used to configure  the mouse. When some mice
	were chosen,  the resulting configuration file was not
	correct.

	The users suggested   that we should have  support for
	swapping in order to  bypass the  memory restrictions.
	(There were some reports of  system crashes because of
	overloading of bitmaps.) The lack of SCSI support was,
	of  course, a big  minus.  It wasn't really physically
	possible to have a large SCSI kernel  on the same disk
	with X - there just isn't enough space on a floppy.

	Last summer Umsdos file system was introduced to Linux
	and  we  began to  think, that   this would be  a good
	starting point.  Recently, a lot of work has been done
	in the Linux community in this  field and the speed of
	this  file system has  doubled.   So, we decided, that
	although it is a kludge, it  is usable to introductory
	purposes and thus also for Xdenu.

	After deciding to collect  a new hard disk version, we
	adapted some new principles, like modularity. So, some
	parts   of the  system   (e.g.  X)  were separated  to
	different upgrade  module  files. Because  we are both
	modem users at the  moment, we collected a term module
	package.

	So,  here it is, in   your hands, a brand new  system!
	Faster  and  more flexible  for  upgrading,  Xdenu^2.0
	(Xdenu squared).

	Users are encouraged to install a full Linux system on
	their computers. After  installing Xdenu the way up is
	easy, but  needs  some careful investigation of  Linux
	document files.

	We wish you good luck. Welcome to the world of Linux!

9.0. Bugs

	Doubtless  many. Feel free to  contact  the authors at
	xdenu@cs.hut.fi.

	Jorma Rinkinen		Jari Miettinen
	jrin@cs.hut.fi		zodiac@heart.hut.fi


10.0. Post Scriptum

	About our future  plans. Well,  we probably fix  Xdenu
	1.0 bug and  make new images. Then we  may make  a few
	more modules for Xdenu 2.0. From then on it depends on
	you, the user.   We have received only one (Christmas)
	card, yet.

	So, if  you find  our terminal package  useful, please
	send us a postcard (this package is a kind of cardware
	:v). You can use Jorma's address:

	Korkeavuorenkatu 7A 8
	00140 Helsinki
	FINLAND

	Thank you and Merry Xmas!