Short introduction to the char package.

The char package is a set of routines to handle coded character
sets and conversions between them. The coded character sets are
described using a short unique name for each character and then
specifying for each coded character set which character is
present at each code point by use of the short character name.

The short character name is mnemonic as far as possible,
and about 1900 mnemonics are defined, plus about 25.000 names
for ideographic characters. All mnemonics are written
in a minimal character set with a repertoire of the ISO 646
invariant character set excluding also the aampersand and the
spece character, that is in all 81 characters.

Coded Character sets are then named, with more than one name
possible for each set, eg. to specify that two standards are
actually the same, or for generality or convenience.
The current package has support for about 140 coded character sets.

Conversion from a coded character set to another is done for 
a character occurring in both sets by just outputting the code point
in the new set. If the character does not occur in the new set,
the mnemonic is output in the coding of the new set, preceded
by a selectable "intro" character.  The "intro" character is
doubled to represent itself. Mnemonics longer than 2 characters
are surrounded by an underline character on both sides.

With the package is distributed some C routines to
do the conversion, namely the getchset() and strncnv() routines.
getchset() establishes an internal structure describing a
character set, given a character set name, and strncnv()
converts a string in one character set to another string in another
character set, with a maximum byte length. The C routines
are written for UNIX systems, but they are made adaptable for other
systems as well, as they do not require any special UNIX facilities.

The code and tables are copyrighted, but with very limited
restrictions on copying.

There is a specification defined in RFC 1345
and the software is partly implementing these internet-drafts.
The current implementation does not handle character sets
or long mnemonics.

Keld Simonsen